## Slide 1: Conferencing with MSRP
draft-niemi-simple-chat-02.txt
Miguel Garcia, Aki Niemi
IETF-62
08-March-2005

## Slide 2: Draft overview
The draft discusses:
Requirements for conferences with MSRP media
Mechanism to do private messaging:
  Proposal for a new DISTSEND MSRP method
  Proposal for new MSRP headers
Nickname representation
Usage of Message/CPIM in MSRP conferences

## Slide 3: Requirements
REQ-4: It must be possible to inform the creator of a session based messaging about the acceptance of the message for distribution.
REQ-5: It must be possible to get the time-stamp at which the MSRP switch dispatched a message.
REQ-6: The message sequence witnessed by different endpoints must be identical across all the participants.
REQ-7: A conference participant must be able to determine the identity or nickname of the creator of the message.
REQ-8: A conference participant must be able to determine the target of the received message. For instance, the message might be addressed to the whole conference, a sidebar conference or just the recipient of the message (private message).
REQ-10: It must be possible to send a message to one or more participants of the conference (private instant message).
REQ-11: A conference participant may have a nickname or pseudonym associated to him.
REQ-14: On sending private messages, it might be possible that the creator sends private messages to participants who have only revealed their nickname, but not their routable SIP URI.

## Slide 4: Send a message to all
Alice sends a regular SEND request that contains a Message/CPIM document.

## Slide 5: Send a private message
Alice sends a DISTSEND request that contains a Distribution header and Message/CPIM document.

## Slide 6: Proposed extensions to MSRP
New DISTSEND method
  Endpoint sends a message to the MSRP switch for further distribution to a subset of the participants.
  Recipient list includes SIP URIs, nicknames, TEL URLs, etc.
  New method required to discover inability of the MSRP switch to do private messaging.
  It always contains a Message/CPIM body.
  Successful report for providing a hint of reception at MSRP switch and a hint of the sequence of message in which this message is inserted.
New Distribution header
  Contains the list of recipients.
  Recipients can be listed with any format, including an ID (SIP URI, TEL URI) or a nickname.
New DateTime header
  Similar to the DateTime header in Message/CPIM.
  Required to get information of the date/time the MSRP switch dispatched a message.
  Avoid the MSRP switch to open Message/CPIM bodies just to insert it in Message/CPIM.

## Slide 7: Nicknames
A nickname is represented as a combination of a Display-Name and a URN.
URNs present two interesting properties.
  URNs are not routable, just names -> allows some anonymity.
  URNs are hierarchical => allows to scope the namespace to that of the conference, MSRP switch, etc.
Nicknames can be learnt from the conference event package.
Nicknames can appear in the From, To, and Cc header of Message/CPIM and the Distribution header in MSRP.
Example of Nickname in Message/CPIM:
From: "Prince of the snow" <urn:ietf:params:msrp:nicknames:com:example:switch:johnny>
Open issue: how to negotiate nicknames to guarantee uniqueness at least within a conference?

## Slide 8: Message/CPIM
From header contains the ID (SIP URI, TEL URI) or nickname of the creator of the message.
To and Cc headers contain a list of visible IDs (SIP URI, TEL URI) or nicknames of the visible recipients.
Invisible recipients are not listed in Message/CPIM (but are just indicated in the Distribution header of DISTSEND).

## Slide 9: Way to move forward
Several components of the draft may fall into the area of different working groups, dependent on the chosen solution.
  General behavior of an MSRP switch, including Message/CPIM usage, and usage of reports.
    XCON + SIMPLE
    DateTime header in MSRP? => Simple
  Sending private messages:
    XCON if a generic solution is chosen and if no impacts to MSRP;
    otherwise, SIMPLE.
  Nicknames:
    SIP/SIPPING if negotiation of a nickname is done in SIP.
    SIMPLE/XCON if we use XCAP to set a nickname.